The GRUB Switch
USB Device Firmware
Ruediger Willenberg
Version 1.0
June 14, 2021
This guide expects that you know how to use the Linux command-line in a console window and are familiar with commands to change directories, list files and start bash scripts. You might also need super user access for some steps, so make sure you have sudo rights.

# About the USB Storage Device firmware
## Licensing
Our USB firmware was modified from code that Atmel Corporation open-sourced for the Application note AVR273: USB Mass Storage Implementation on megaAVR with USB.
The majority of original code was left intact or only has minor modifications and is under an Atmel-specific “Use with attribution”-style license, whose only major restriction is that the code can only be used in connection with Atmel devices. It MAY NOT be ported to other microcontroller architectures from competing vendors.
NOTE: Atmel has been part of Microchip Technology Inc. since 2016.
Only the source files added by The GRUB Switch project are under an MIT license:
2_usb_device/boards/*
2_usb_device/lib_mem/cf/bootfile_template.S
2_usb_device/lib_mem/cf/boot_choice.h
2_usb_device/lib_mem/cf/boot_choice.c
2_usb_device/lib_mem/cf/fat12_data.h
2_usb_device/lib_mem/cf/fat12_data.c
## Functionality
A board properly programmed the firmware appears as a flash drive on plugging it in. Specifically, it identifies as a drive with one FAT12 partition (the format used on old DOS floppy disks) with the minimum possibly capacity of 33792 bytes (66 sectors of 512 byte). This minimizes management effort and is perfectly sufficient for our purpose.
Files can not be randomly written to the drive, not even below that stated capacity. In fact, the drive will always show exactly 3 files:
.entries.txt is the only file that can actually be written, which is done to write a new boot configuration (a list and order of boot choices or entries and some display parameters) onto the board. The data is stored in the chips EEPROM, which has 1KByte or 2 sectors of capacity. However, entry files can actually not be larger than 960 bytes (which is sufficient for all practical cases), as we reserve 64 bytes for other stored parameters.
With an external pin, the board can be put into Write Protect mode, and then even .entries.txt is read-only to protect the boot entries from tampering.
.bootpins.txt is a read-only file that is generated on opening/reading and display the state of the boards boot choice pins, depending on the configured choice mode:
- In 1-of-n mode, which is the default, the file indicates with a 1 which pins have been tied to GND, the lowest one making the boot choice. The following example shows a situation where choice pin 3 has been connected:
  11->1: 00000000100
- In binary mode, which can be activated through another board pin, only the first 4 choice pins are sampled and connections are interpreted as powers-of-two 1,2,4,8. The following example shows a situation where the lower three pins have been connected to GND, resulting in a boot choice of 7:
  Binary pick: 0111
SWITCH.GRB is the only file that is not declared “hidden” by either FAT attributes (for Windows) or a leading period (for Linux). It is another read-only, dynamically generated file and it’s content depends on the boot choice pins, the choice mode and the content of .entries.txt. It can be sourced on boot by the GRUB infrastructure as a script and will set a new default GRUB menu entry and a menu wait time of 0 seconds, therefore forcing the GRUB menu choice. If boot choice pins indicate no connection (choice 0), the file is empty and the GRUB menu is not cut off.
As to make sure that the PC is not buffering or caching an old version of SWITCH.GRB, the board will disconnect from the USB host and reconnect right away whenever a board pin changes state (including on change of the Write Protect status), forcing the PC to read the changed SWITCH.GRB

Because the file structure does not change except for the size of .entries.txt, almost the entire File Allocation Table (FAT) is immutable and actually stored in code flash memory.

# How to build the firmware yourself
## Prerequisites
The device firmware is intended to be built with the free GNU toolchain under Linux (though it can be made to work on other OSes). At the minimum, you need to install the packages for the GCC AVR compiler and the AVR standard libraries, for example under Ubuntu with
sudo apt-get install gcc-avr
sudo apt-get install avr-libc
Further tools are needed to program various boards (see below)

If you have not already downloaded the GRUB Switch repository itself, there are two ways to obtain it:
- Via git clone:
  - Go to your preferred working directory
  - Clone the repository with
    git clone https://github.com/rw-hsma-fpga/grub-switch.git
  - All GRUB Switch files are now available in the path
    ./grub-switch
- Via download:
  - Download to your preferred directory:
    https://github.com/rw-hsma-fpga/grub-switch/archive/refs/heads/master.zip
  - Unzip with GUI-tool or on the command line with
    unzip grub-switch-master.zip
  - All GRUB Switch files are now available in the path
    ./grub-switch-master

All further examples will assume you are starting in the parent directory above grub-switch
## Building firmware images
The root directory for the device firmware can be entered with
cd grub-switch/2_usb device/
For a first run at building the firmware, just call make:
make
A successful run should indicate that an image for the TEENSY20 (Teensy 2.0 board) has been built, as that is the default set in the Makefile. Three files are being generated in the local directory: An ELF file, a file in Intel Hex format and a memory map report. Generally, *.hex files will be used for device programming:
GRUB_SWITCH_TEENSY20.elf	GRUB_SWITCH_TEENSY20.hex
GRUB_SWITCH_TEENSY20.map
Furthermore, all intermediate build files can be found in the ./build/ subdirectory. To remove all generated files again (including the ones in ./build/ ), call
make clean
To build for another target board, specify the BOARD parameter:
make BOARD=TARGETBOARD
The target board name is always a capitalized version of the corresponding board header file that can be found in ./boards/include/ . As an example, the header file for the Arduino Micro is ./boards/include/arduino_micro.h and the image for it is built with
make BOARD=ARDUINO_MICRO
which generates
GRUB_SWITCH_ARDUINO_MICRO.elf	GRUB_SWITCH_ARDUINO_MICRO.hex
GRUB_SWITCH_ARDUINO_MICRO.map
There is a bash script to auto-generate all images with corresponding headers in ./boards/include/, which can be called with
./make_all_boards
If you want to store the generated images as prebuilt images, you have to hand-copy them to the ./prebuilt_images/ directory with
cp *.hex ./prebuilt_images
Do not delete the ./prebuilt_images/ directory even when you want to re-generate all images, as it also holds bash scripts for programming the images onto the boards.
# Adding a new board as a build target
The device firmware sources are designed to make it easy to add support for another new board with the ATmega32u4 chip. With proper information in the form of a schematic, you only need to copy, rename and modify one file and add a line to another. For both actions you should go to the 2_usb_device/boards/include/ path, for example with:
cd grub-switch/2_usb_device/boards/include
## Making a board header file and changing named tokens
The best way to produce a valid header file for your board is to copy an existing file and modify it properly. Let’s say you board is called Foobar+ and we’re using the Arduino Micro header file as a template, then you start with
cp arduino_micro.h foobar_plus.h
Open the file with your favored text editor, for example
nano foobar_plus.h
You should then change all capitalized mentions of ARDUINO_MICRO in tokens to capitalized FOOBAR_PLUS, so the following lines at various positions in the file
#ifndef ARDUINO_MICRO_H
#define ARDUINO_MICRO_H
#ifdef TARGET_BOARD_ARDUINO_MICRO
#endif // TARGET_BOARD==ARDUINO_MICRO
#endif // ARDUINO_MICRO_H
should turn into
#ifndef FOOBAR_PLUS_H
#define FOOBAR_PLUS_H
#ifdef TARGET_BOARD_FOOBAR_PLUS
#endif // TARGET_BOARD==FOOBAR_PLUS
#endif // FOOBAR_PLUS_H
The comments are not strictly necessary, of course, it’s just proper code structure.
## Adjusting the clock frequency (relates to supply voltage)
ATmega32u4 MCUs serving as a USB device need one of two external crystals or oscillators:
- If the chip is supplied with a VCC of +5V, it needs to be clocked with 16MHz
- If the chip is supplied with a VCC of +3.3V, it needs to be clocked with 8MHz
There are no other combinations of supply voltage and external frequency that work. The internal oscillator in the -RC versions of the chip is not accurate enough for the USB timing.
The chip sadly does not autodetect its environment and needs to be told which divider to use for its USB timing (therefore there are some boards like the Pro Micro that have almost identical 3V and 5V version, but they need this one different value in their firmware image.
You need to set the FOSC macro in the header file to the proper clock value in kHz:
#define FOSC 8000 // for 8MHz clocking (VCC=+3.3V)
or
#define FOSC 16000 // for 16MHz clocking (VCC=+5V)
## Pin assignments
ATmega32u4 names all it’s port pins with digital GPIO capability with letter/digit combinations starting from PB0 up to PF7. They are almost multiplexed with other pin functions, but a specific board will usually only expose those GPIO pins as I/O solder pads that are not required to operate as something else.
Every board will have a different set and order of exposed pins and it is up the header file writer to put the required GRUB Switch functions into a practical order (if in doubt, look at the pinout assignments and switching diagrams for the already supported boards). The pads might also use other naming schemes, like the Arduino one, so you DO need a schematic to be sure which pad is connected to which MCU pin.
For each pin function we want to declare, we have defined a pair of macros FUNCTION_PORT and FUNCTION_PIN that require you to separately specify the letter (port) and the digit (pin) of the assigned pin.
All pins defined for input functions (pin level sampled by the firmware for some purpose) have a pull-up resistor activated so that they are by default a logical high-level (1). This way both input levels can be chosen by connecting it to 0V/GND (0) or leaving it unconnected (1).
### Setting the LED pin and active level
Most boards have at least one LED that can be switched by a GPIO pin. Our firmware uses that LED to indicate the writing of a new boot configuration (which can take up to 2 seconds) and it also flashes briefly on USB power-up.
On the Arduino Micro, the LED is connected to Pin PC7, so the definitions look like this:
#define LED_PORT C
#define LED_PIN 7
(The P for port is left out) You need to adjust this to the letter/number combination for your board’s LED port.
Boards can also differ in whether the LED lights up on a high level (1) or a low level (0) output. On most boards, the former is true: The LED’s anode is connected to the pin, and the cathode is tied to 0V (there’ll be a series resistor somewhere). But on some boards, the LED’s cathode is connected to the pin and the anode is tied to VCC. If that is the case, you need to add and extra definition
#define LED_IS_LOW_ACTIVE
and the firmware will make the proper adjustment.
### /WR_PROT and /BINARY_MODE pins
Two other special pin functions are required for proper firmware operation.
If the /WR_PROT pin is tied to low-level/0V/GND, the firmware doesn’t allow to overwrite the current boot configuration file. If it’s left unconnected, changing the boot configuration is possible. Our Arduino Micro configuration uses PF6, so the macros are
#define WRPROT_PORT F
#define WRPROT_PIN 6
Adjust accordingly to your preferred Write-Protect pin.
When the /BINARY_MODE pin is tied to low-level/0V/GND, the firmware interprets the first four choice pins (see below) as a binary number, therefore enabling boot choices from 0..15 (0x0..0xF). If the pin is unconnected, the firmware uses the default 1-of-n mode. Our Arduino Micro configuration uses PF1, so the macros are
#define MODE_PORT F
#define MODE_PIN 1
Adjust accordingly to your preferred Binary mode pin.
### Auxiliary low-level(0V) pins.
It is often helpful to have the /WR_PROT and /BINARY_MODE pads neighbouring a 0V/GND pad, so a jumper or a short solder bridge can be used to activate either function. However, GND pads are limited in number and this is not always feasible. We have therefore defined two macro pairs that make regular GPIO pins outputs that are permanently set to low-level/0V. They can then be used to tie down the mode pins, or even connect the choice pins (see below) to them instead of to a real 0V/GND pad. Our Arduino Micro configuration uses PF7 and PF0, which are indeed adjacent to /WR_PROT and /BINARY_MODE on that board:
#define AUX0_PORT1 F
#define AUX0_PIN1 7
#define AUX0_PORT2 F
#define AUX0_PIN2 0
Adjust accordingly to your pins. If you don’t need two such pins and are running out of otherwise unused MCU pins, you can even both declare them to the same location without any harm (the output direction and 0-value is just set twice).
### Choice pins
Up to 11 pins can be declared to indicate boot choices by tying them to 0V/GND. For the default 1-of-n-mode (/BINARY_MODE not active), the lowest-order pin tied to 0 indicated the boot choice; if no choice pin is connected, GRUB Switch goes to the GRUB menu. In Binary mode (/BINARY_MODE tied to 0), only the choice pins 1..4 are read and interpreted as powers of two 1,2,4,8 when they’re tied to GND.
Our Arduino Micro configuration uses 11 pads from PD1 to PD6 for these choice pins:
#define CHOICE_PORT1 D
#define CHOICE_PIN1 1
#define CHOICE_PORT2 D
#define CHOICE_PIN2 0
[…]
#define CHOICE_PORT10 B
#define CHOICE_PIN10 7
#define CHOICE_PORT11 D
#define CHOICE_PIN11 6
Adjust accordingly to your board’s pad order. If not enough pins or pads are free for 11 choices, all the upper choices can be assigned to the same pin with no harm (it should of course be unconnected, and all these choices will then never be selected).
We recommend again to look at the connection patterns and assignments for the boards that are already supported for inspiration. They can be found in the Quickstart.pdf as well as in the form of ASCII text files in the ./boards/ directory.
When all the modifications have been made and checked again, you can save the new header file.
## Add header file to boards.h
Open the existing file 2_usb_device/boards/include/boards.h with your favourite text editor, e.g.
nano boards.h
and add your new header file to the list of includes, for example
#include "boards/include/foobar_plus.h"
Save and close the file. The adding process is finished. After returning to the 2_usb_device directory with
cd ../../
it should now be possible to compile the new firmware by specifying the new board code in capitalized form, for example
make BOARD=FOOBAR_PLUS
which will produce the requisite ELF, HEX and MAP files. Because our bash script parses the boards.h file, calling
./make_all_boards
will also include a build for the new board’s firmware image.

# Selecting and ordering your boot choices
Choose menu option 2 to start the actual GRUB Switch configuration.
The tool will show a complete list of boot choices in the order extracted from the GRUB configuration. Moving up and down with the cursor keys, you can use number keys (and the hexadecimal letters a to f representing 10..15) to assign choices a position in the GRUB Switch selection order.

Not all entries have to be chosen and assigned a numerical position. The Enter key continues to the next screen.
The next screen shows the selected choices and position assignments. They can be confirmed with the Enter key; the Backspace key returns to the previous screen for further changes.

It is possible to display the chosen boot option for a number of seconds, which can be adjusted in the next tool screen. If you keep or set the value to 0 seconds, there will be no choice display. The operating system selected by GRUB Switch will be booted instantly.

The last configuration screen allows choosing a highlight color (foreground/background) for the choice display. Enter finishes the boot configuration. A final screen shows the output written into the configuration file grub-switch/bootfiles/.entries.txt, which is used to configure the switchable USB storage device.

After pressing a key, the tool returns to the main screen. The status of generated bootfiles shows that they have just been generated.
To clean up, the generated files can be deleted with menu option 3.
## Storing hash values for boot choice authentication
For every generated boot file, a unique SHA512 hash sum been generated. By selecting action 5, these hashes can be stored into the system’s boot directory. As this option writes into the boot path, both sudo rights authorization and an extra confirmation are required:

When such hashes have been installed, GRUB Switch will only execute boot options for which it finds corresponding hash sums. This mechanism protects the system against flash drives with unauthorized GRUB scripts.

The hashes can be removed again from the boot directory with option 6.
IMPORTANT NOTE: Some Linux distributions install updated versions of GRUB where not all submodules have an UEFI Secure Boot signature (I’m looking at you, Kubuntu 18.04). If you have an UEFI BIOS with Secure Boot enabled, GRUB Switch will give you an error on trying to use the hash module and will boot through the regular GRUB menu. If this happens, you have three possible fixes:
- Remove the hash sums again with option 6 (most simple).
- Disable Secure Boot in BIOS (consider first if Secure Boot is really optional for you).
- Roll back any updates to GRUB to the signed version (most complicated).
# Adding GRUB Switch to your GRUB installation
Before your generated boot choice files can have any impact, you need to install the actual GRUB Switch modification to GRUB. This is accomplished with action 7 in the tool:
This action also requires sudo write rights and an additional confirmation:

File status will show the installed GRUB Switch modification:

IMPORTANT: GRUB Switch needs to be installed ONLY ONCE, not every time you change the boot choices and generate new files. If you have downloaded a newer version of GRUB Switch where the GRUB modifications have changed, the file status will indicate this and you can reinstall.
GRUB Switch can be removed again with menu option 8.
# Method A to use GRUB Switch: Using regular USB flash drives for boot choice
Picking and configuring boot entries with option 2 in the CONFIGURE_GRUBswitch.sh tool has generated directories and files like these in your directory grub-switch/bootfiles :
bootfiles/boot.1/SWITCH.GRB
bootfiles/boot.2/SWITCH.GRB
bootfiles/boot.2/SWITCH.GRB
You will find boot.* dirs according to the positions you assigned during configuration. There won’t be a boot.0 dir because that choice is reserved for the GRUB menu. Each directory holds a SWITCH.GRB file that sets the variable for the corresponding boot choice when called by GRUB. You can open it with a text editor, though I don’t recommend editing it by hand.
You will now need as many USB flash drives as you have picked boot choices (excluding the GRUB menu).
- Make sure each flash drive is formatted with a FAT file system (FAT12/16/32, exFAT, VFAT), not with NTFS or any other file system.
  You do not need to re-format an existing drive, or even delete its files (although you might want to for reasons of cleanliness, data protection, privacy, etc.).
- Copy each SWITCH.GRB file to a separate flash drive and mark the drive with the corresponding number, OS name or whatever helps you tell them apart.
- Before powering on your computer or rebooting, plug in the flash drive representing your boot choice.
- If you want the GRUB menu to appear, make sure none of the drives are plugged in.
- If multiple of your drives are plugged in by accident, boot choice will depend on the ordering of USB connections in your BIOS, which you might not be able to tell easily.

All further chapters are not relevant if you stick with this method to make your boot choice.
# Method B to use GRUB Switch: Using hardware switches and a programmable USB board for boot choice
If you want to make your boot choice through an electromechanical switch, you need to use a programmable USB board, flash it with our firmware and connect a suitable switch to it.
Our firmware is designed for boards with the Microchip/Atmel ATmega32u4 chip, which can act as a USB device. All related files can be found in grub-switch/2_usb_device
## Supported boards
Currently the project includes pre-built firmware images for the following products:
- PJRC Teensy 2.0
- Arduino Micro
- SparkFun Pro Micro (3V and 5V versions) and various clones
- Adafruit ItsyBitsy 32u4 (3V and 5V versions)
- DFRobot Beetle
- Our self-designed, non-commercial Custom Hardware PCB (see 5.2.3)
It is fairly simple to adapt the firmware to another board with the ATmega32u4 and build a firmware image. See the detailed documentation for instructions.
## Programming the boards with GRUB Switch firmware
On the Linux command-line, go to the grub-switch/2_usb_device/prebuilt_images directory, where you can find the suitable image and programming scripts.
### Teensy 2.0
Teensy 2.0 has a proprietary bootloader which works with its own GUI programming tool, Teensy Loader. You can find precise installation and download instructions here:
https://www.pjrc.com/teensy/loader_linux.html
The corresponding image is prebuilt_images/GRUB_SWITCH_TEENSY20.hex
### Arduino-compatible boards
Arduino Micro, ItsyBitsy, Pro Micro and Beetle all use a bootloader that is compatible with Arduino IDE, however the IDE does not have an option for downloading any random *.hex file. We therefore require a command-line tool called avrdude, which is available in many Linux repositories.
- Under Ubuntu, for example, you can install avrdude with

  sudo apt-get install avrdude
- To simplify the use of avrdude, we have provided a script in prebuilt_images. After plugging in your board, it can be started with:

  sudo ./program_grubswitch_avrdude.sh CORRECT_FIRMWARE.hex

  (The use of sudo might not be required on your installation)
- The script will ask you to put the connected board into bootloader mode:
  - For the Arduino Micro and ItsyBitsy bootloader mode can be entered by pushing the board’s reset button twice.
  - The Pro Micro does not have a reset button; you have to short the GND and RST pads twice in short order with a wire.
  - The Beetle has a group of 6 tiny pads on the bottom side below its USB socket:
    1 3 5
    # O O Pad number 1 is square, not round.
    O O O Short the round pads number 5 and 6 twice in
    2 4 6 short order to put Beetle into bootloader mode
- After putting your board into bootloader mode, you have between 5 and 10 seconds to press a keyboard key for the programming script to continue; any longer, and the board leaves bootloader mode again.
After successful firmware programming, the board identifies as a FAT12 storage device. Depending on your Linux GUI, you might get a device notification.
NOTE: There are separate firmware images for the 3V and 5V versions of both ItsyBitsy and Pro Micro, as they need different oscillator configurations. Downloading the wrong firmware will not cause harm, the firmware will just not function. The board can be brought into bootloader mode again, and reprogrammed with the correct firmware.
### THE GRUB SWITCH custom USB hardware Rev.B
Our custom USB device design relies on the DFU bootloader which is factory-built into each ATmega32u4 chip. There is an open source command-line tool called dfu-programmer which needs to be installed for firmware flashing.
- Under Ubuntu Linux, it can be installed with:
  sudo apt-get install dfu-programmer
- To simplify the use of dfu-programmer, we have provided a script in prebuilt_images. After plugging in your board, it can be started with:
  sudo ./program_grubswitch_dfu.sh GRUB_SWITCH_CUSTOMHW_REVB.hex
  (The use of sudo might not be required on your installation)
- Before or after starting the script, the chip needs to be brought into bootloader mode by pushing or shorting the PROG button. Unlike the Arduino boards, there is no bootloader timeout. Pressing a key on the keyboard will start programming.
After successful firmware programming, the board identifies as a FAT storage device with the drive name BOOTTHIS. Depending on your Linux GUI, you might get a notification.
## Writing the GRUB Switch boot configuration onto your storage device
Together with the boot.* directories, option 2 of the CONFIGURE_GRUBswitch.sh script has also written a single text file holding the complete list and order of boot choices:
bootfiles/.entries.txt
You can open with a text editor to see the ordered list of boot choices, however it is not recommended to edit the file by hand. Because the filename starts with a period, it is only visible if you use the -a option with ls:
ls -la bootfiles/
If you mount your USB storage device automatically through the GUI, you can just copy the file onto the device and unmount again.
Alternatively, you can use option 4 - Write GRUBswitch bootfile to GRUBswitch USB device in the CONFIGURE_GRUBswitch.sh tool. This requires giving the sudo password because the mounting and unmounting of the device is being forced.
NOTE: Your USB device is not a regular flash drive. .entries.txt is the only file that will be accepted for writing, and only if the Write-Protect jumper is not set on the board (see wiring section). The only other (read-only) files on the device are:
SWITCH.GRB – The actual boot setting script read by GRUB. If there are no switch connections on the board yet, this will be empty because that is the default leading to the GRUB menu.
.bootpins.txt – This file (also hidden without ls -a) shows the choice pins currently connected to GND as ones. It is only included for testing purposes.
## Electrical connections to the GRUB Switch boards
There are multiple ways to connect switches to each board to control the boot choice.
### Arduino Micro