The GRUB Switch - Quickstart Guide
Ruediger Willenberg
Version 1.8
April 29, 2023
Note: The GRUB Switch only works with GRUB 2.x, not the outdated GRUB Legacy
This guide expects that you know how to use the Linux command-line in a console window and are familiar with commands to change directories, list files and start bash scripts. You will also need super user access for some steps, so make sure you have sudo rights.
Refer to the detailed documentation if these quick steps do not work on your platform.
# Preliminary steps to take for GRUB v2.06 and higher
Starting with GRUB version 2.06 which was released in 2022, Windows and Linux installations on other partitions are not guaranteed to be included in the GRUB boot menu.
To find out if GRUB v.2.06 or higher is installed, call
grub-install --version
If the version is 2.06 or higher, we need to modify the parameter file /etc/default/grub that controls how the GRUB menu is assembled. Open the file with a text editor with root rights, for example with
sudo nano /etc/default/grub
Add the line
GRUB_DISABLE_OS_PROBER=false
and save the file. Afterwards, run update-grub at least once to rebuild the GRUB menu with
sudo update-grub
before using our GRUB Switch command-line tools as detailed below.
# Downloading and installing GRUB Switch repository
The GRUB Switch scripts and files are designed to be installed and used under Linux. There are two ways to obtain the files:
- Via git clone:
  - Go to your preferred working directory and clone the repository with
    git clone https://github.com/rw-hsma-fpga/grub-switch.git
  - All GRUB Switch files are now available in the path
    ./grub-switch
- Via download:
  - Download to your preferred directory:
    https://github.com/rw-hsma-fpga/grub-switch/archive/refs/heads/master.zip
  - Unzip with GUI-tool or on the command line with
    unzip grub-switch-master.zip
  - All GRUB Switch files are now available in the path
    ./grub-switch-master
All further examples will assume you are starting in the parent directory above grub-switch
# Configuring your boot choices
To configure your GRUB Switch boot choices, enter the bash script directory with
cd grub-switch/1_shell_scripts/
(exact path depends on your installation location and current working directory)
Start the configuration tool with
./CONFIGURE_GRUBswitch.sh
Do not start the configuration tool with sudo or all generated files will be owned by root. The script asks for sudo once right after you start it, and uses it when super user rights are required. You may be asked again when sudo privileges time out.

The main screen then should appear as above (depending on your console theme).
Below that, the script lists the status of important files either required or generated by this tool.
In the lower half, the tool offers a menu of actions to take by pressing a corresponding number key.
## Extracting a list of GRUB menu entries
By choosing option 1, the tool will parse GRUB’s menu configuration file and generate a local text file grub-switch/bootfiles/grubmenu_all_entries.txt that lists all menu entries, including ones in submenus, and is the basis for picking your custom boot choices.
Before the extraction, you have the option to re-generate the grub.cfg with update-grub so that your extracted choices reflect the most recent boot options. This is generally recommended, with the exception of Linux Mint (see section on specific Linux distributions).
After returning to the main screen, the status of grubmenu_all_entries.txt should reflect the recent extraction date.
## Selecting and ordering your boot choices
Choose menu option 2 to start the actual GRUB Switch configuration.
The tool will show a complete list of boot choices in the order extracted from the GRUB configuration. Moving up and down with the cursor keys, you can use number keys (and the hexadecimal letters a to f representing 10..15) to assign choices a position in the GRUB Switch selection order.

Not all entries have to be chosen and assigned a numerical position. The Enter key continues to the next screen.
The next screen shows the selected choices and position assignments. They can be confirmed with the Enter key; the Backspace key returns to the previous screen for further changes.

Before booting, the chosen boot option will be displayed for a number of seconds, which can be adjusted in the next tool screen. The minimum selectable time is 2 seconds, so that there will always be a chance to reach the GRUB menu with the Escape key.

The last configuration screen allows choosing a highlight color (foreground/background) for the choice display. Enter finishes the boot configuration. A final screen shows the output written into the configuration file grub-switch/bootfiles/.entries.txt, which is used to configure the switchable USB storage device.

After pressing a key, the tool returns to the main screen. The status of generated bootfiles shows that they have just been generated.
To clean up, the generated files can be deleted with menu option 3.
## Storing hash values for boot choice authentication
For every generated boot file, a unique SHA512 hash sum been generated. By selecting action 5, these hashes can be stored into the system’s boot directory. As this option writes into the boot path, both sudo rights authorization and an extra confirmation are required:

When such hashes have been installed, GRUB Switch will only execute boot options for which it finds corresponding hash sums. This mechanism protects the system against flash drives with unauthorized GRUB scripts.

The hashes can be removed again from the boot directory with option 6.
IMPORTANT NOTES:
1. Even on Linux distributions that work with UEFI Secure Boot (only standard Ubuntu and openSUSE “Leap” in our tests), the GRUB hash module will NOT work with Secure Boot. We blame this on how GRUB loads the hash module. You’ll have to decide whether to disable Secure Boot or to remove hash checks again with option 6.
2. Hash checking should not be used at all with Fedora Linux, as using the hash function there fails but returns SUCCESS (implying ANY SWITCH.GRB file is OK’d).
3. The same is true of openSUSE if you install it with the default btrfs file system. Hash checking currently works if you install openSUSE on an ext4 partition.
# Adding GRUB Switch to your GRUB installation
Before your generated boot choice files can have any impact, you need to install the actual GRUB Switch modification to GRUB. This is accomplished with action 7 in the tool:
This action also requires sudo write rights and an additional confirmation:

File status will show the installed GRUB Switch modification:

IMPORTANT: GRUB Switch needs to be installed ONLY ONCE, not every time you change the boot choices and generate new files. If you have downloaded a newer version of GRUB Switch where the GRUB modifications have changed, the file status will indicate this and you can reinstall.
GRUB Switch can be removed again with menu option 8.
# Problems with specific Linux distributions
## Linux Mint
Linux Mint is based on Ubuntu and uses a somewhat problematic mechanism to generate its individualized boot entries. When update-grub is called, it actually generates a grub.cfg with menu entries named Ubuntu. Then, every time the PC shuts down or reboots,a script is called that substitutes every mention of Ubuntu with Linux Mint.
As a consequence, you should extract menu entries right after rebooting and without calling update-grub before (which is optional). This way, the extracted entries contain Linux Mint and will be recognized on the next boot.
## Elementary OS
Elementary OS puts its grub.cfg into a different location; this location needs to be specified when starting the GRUB Switch configuration:
./CONFIGURE_GRUBswitch.sh -g /boot/efi/EFI/ubuntu/grub/
(Note: To heighten confusion, the regular location /boot/grub/grub.cfg is also maintained and updated by Elementary OS, however it is not actually used when GRUB is booting)
## Fedora Linux
Fedora uses entry titles that include the kernel version. Therefore, regularly update and
re-extract boot choices to boot the most current kernel version with The GRUB Switch.
Lastly, checking hashes with GRUB Switch does not currently work in Fedora, and unfortunately returns a success value, implying the hash check recognized the file. Please do not use hash checking with Fedora!
## openSUSE
openSUSE’s hash checking also fails by returning success values everytime IF it is installed with the default btrfs file system. If you install openSUSE on an ext4 partition instead, hash checking works.
# Method A to use GRUB Switch: Using regular USB flash drives for boot choice
Picking and configuring boot entries with option 2 in the CONFIGURE_GRUBswitch.sh tool has generated directories and files like these in your directory grub-switch/bootfiles :
bootfiles/boot.1/SWITCH.GRB
bootfiles/boot.2/SWITCH.GRB
bootfiles/boot.2/SWITCH.GRB
You will find boot.* dirs according to the positions you assigned during configuration. There won’t be a boot.0 dir because that choice is reserved for the GRUB menu. Each directory holds a SWITCH.GRB file that sets the variable for the corresponding boot choice when called by GRUB. You can open it with a text editor, though I don’t recommend editing it by hand.
You will now need as many USB flash drives as you have picked boot choices (excluding the GRUB menu).
- Make sure each flash drive is formatted with a FAT file system (FAT12/16/32, exFAT, VFAT), not with NTFS or any other file system.
  You do not need to re-format an existing drive, or even delete its files (although you might want to for reasons of cleanliness, data protection, privacy, etc.).
- Copy each SWITCH.GRB file to a separate flash drive and mark the drive with the corresponding number, OS name or whatever helps you tell them apart.
- Before powering on your computer or rebooting, plug in the flash drive representing your boot choice.
- If you want the GRUB menu to appear, make sure none of the drives are plugged in.
- If multiple of your drives are plugged in by accident, boot choice will depend on the ordering of USB connections in your BIOS, which you might not be able to tell easily.

All further chapters are not relevant if you stick with this method to make your boot choice.
# Method B to use GRUB Switch: Using hardware switches and a programmable USB board for boot choice
If you want to make your boot choice through an electromechanical switch, you need to use a programmable USB board, flash it with our firmware and connect a suitable switch to it.
Our firmware is designed for boards with the Microchip/Atmel ATmega32U4 and ATmega16U4 chips, which can act as a USB device. All related files can be found in
grub-switch/2_usb_device
## Supported boards
Currently the project includes pre-built firmware images for the following products:
- PJRC Teensy 2.0
- Arduino Micro
- SparkFun Pro Micro (3V and 5V versions) and various clones
- Adafruit ItsyBitsy 32u4 (3V and 5V versions)
- DFRobot Beetle
- Our self-designed, non-commercial Custom Hardware PCB (see 5.4.6)
It is fairly simple to adapt the firmware to another board with the ATmega32U4/16U4 and build a firmware image. See the detailed documentation for instructions.
## Programming the boards with GRUB Switch firmware
On the Linux command-line, go to the grub-switch/2_usb_device/prebuilt_images directory, where you can find the suitable image and programming scripts.
### Teensy 2.0
Teensy 2.0 has a proprietary bootloader which works with its own GUI programming tool, Teensy Loader. You can find precise installation and download instructions here:
https://www.pjrc.com/teensy/loader_linux.html
The corresponding image is prebuilt_images/GS_TEENSY20.hex
### Arduino-compatible boards
Arduino Micro, ItsyBitsy, Pro Micro and Beetle all use a bootloader that is compatible with Arduino IDE, however the IDE does not have an option for downloading any random *.hex file. We therefore require a command-line tool called avrdude, which is available in many Linux repositories.
- Under Ubuntu, for example, you can install avrdude with

  sudo apt-get install avrdude
- To simplify the use of avrdude, we have provided a script in prebuilt_images. After plugging in your board, it can be started with:

  sudo ./program_grubswitch_avrdude.sh CORRECT_FIRMWARE.hex

  (The use of sudo might not be required on your installation)
- The script will ask you to put the connected board into bootloader mode:
  - For the Arduino Micro and ItsyBitsy bootloader mode can be entered by pushing the board’s reset button twice.
  - The Pro Micro does not have a reset button; you have to short the GND and RST pads twice in short order with a wire.
  - The Beetle has a group of 6 tiny pads on the bottom side below its USB socket:
    1 3 5
    # O O Pad number 1 is square, not round.
    O O O Short the round pads number 5 and 6 twice in
    2 4 6 short order to put Beetle into bootloader mode
- After putting your board into bootloader mode, you have between 5 and 10 seconds to press a keyboard key for the programming script to continue; any longer, and the board leaves bootloader mode again.
After successful firmware programming, the board identifies as a FAT12 storage device. Depending on your Linux GUI, you might get a device notification.
NOTE: There are separate firmware images for the 3V and 5V versions of both ItsyBitsy and Pro Micro, as they need different oscillator configurations. Downloading the wrong firmware will not cause harm, the firmware will just not function. The board can be brought into bootloader mode again, and reprogrammed with the correct firmware.
### THE GRUB SWITCH custom USB hardware
Our custom USB device design relies on the DFU bootloader which is factory-built into each ATmega32U4/16U4 chip. There is an open source command-line tool called dfu-programmer which needs to be installed for firmware flashing.
- Under Ubuntu Linux, it can be installed with:
  sudo apt-get install dfu-programmer
- To simplify the use of dfu-programmer, we have provided a script in prebuilt_images. After plugging in your board, it can be started with:
  sudo ./program_grubswitch_dfu.sh GS_CUSTOMHW_REVC_32U4.hex
   or
  sudo ./program_grubswitch_dfu.sh GS_CUSTOMHW_REVC_16U4.hex
  depending on the chip used on the board.
  (The use of sudo might not be required on your installation)
- Before or after starting the script, the chip needs to be brought into bootloader mode by pushing or shorting the PROG button. Unlike the Arduino boards, there is no bootloader timeout. Pressing a key on the keyboard will start programming.
After successful firmware programming, the board identifies as a FAT storage device with the drive name BOOTTHIS. Depending on your Linux GUI, you might get a notification.
## Writing the GRUB Switch boot configuration onto your storage device
Together with the boot.* directories, option 2 of the CONFIGURE_GRUBswitch.sh script has also written a single text file holding the complete list and order of boot choices:
bootfiles/.entries.txt
You can open with a text editor to see the ordered list of boot choices, however it is not recommended to edit the file by hand. Because the filename starts with a period, it is only visible if you use the -a option with ls:
ls -la bootfiles/
If you mount your USB storage device automatically through the GUI, you can just copy the file onto the device and unmount again.
Alternatively, you can use option 4 - Write GRUBswitch bootfile to GRUBswitch USB device in the CONFIGURE_GRUBswitch.sh tool. This requires giving the sudo password because the mounting and unmounting of the device is being forced.
NOTE: Your USB device is not a regular flash drive. .entries.txt is the only file that will be accepted for writing, and only if the Write-Protect jumper is not set on the board (see wiring section). The only other (read-only) files on the device are:
SWITCH.GRB – The actual boot setting script read by GRUB. If there are no switch connections on the board yet, this will be empty because that is the default leading to the GRUB menu.
.bootpins.txt – This file (also hidden without ls -a) shows the choice pins currently connected to GND as ones. It is only included for testing purposes.
## Electrical connections to the GRUB Switch boards
There are multiple ways to connect switches to each board to control the boot choice.
### Arduino Micro
1-OF-N MODE with ON/OFF/ON toggle switch:
-------------------------------------------

To choose this mode, pin PF1 needs to stay UNCONNECTED.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PF6 to GND or PF7 (adjacent pad, driving a low level).

Using a three-position on/off/on switch permits choosing between two
OS options, while the neutral middle position leads to the GRUB menu

        ##### [1]
        .-----------o=# # ////
        | # #|| ////
        | .---o=# #||//// [0] Menu
        | | # #||
        | .---|---o=# #
        | | | ##### [2]
        | | |
        | | |
.--------------------------------------+---+---+-----------------------.
| O O O O O O O O O O O O O O O O O |
| 12 11 10 9 8 7 6 5 4 3 2 GND RST RX TX SS MOSI |
| PD6 PB7 PB6 PB5 PB4 PE6 PD7 PC6 PD4 PD0 PD1 PD2 PD1 PB0 PB2 |
| |
| |
|=========# |
| USB # |
| # ARDUINO MICRO |
| MICRO-B # |
|=========# |
| |
| |
| PC7 PF7 PF6 PF5 PF4 PF1 PF0 PB3 PB1 |
| 13 3V3 AREF A0 A1 A2 A3 A4 A5 5V0 RST GND VIN MISO SCK |
| O O O O O O O O O O O O O O O O O |
'--------------+---+---------------------------------------------------'
        | |
        | |
        ?
        /WR_PROT

1-OF-N MODE with rotary switch: (Motto: "This one goes to 11!")
---------------------------------------------------------------

To choose this mode, pin PF1 needs to stay UNCONNECTED.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PF6 to GND or PF7 (adjacent pad, driving a low level).

Common rotary switches have up to 12 positions (some can be limited to fewer
positions with a mechanical keyring). Keeping the first position [0] unconnected
permits choosing the GRUB menu and leaves 11 boot choices, which is the maximum
number of pins sampled. Connecting one of the pins PD1..PD6 to GND
therefore reflects boot choices 1..11 (hexadecimal 0x1..0xB). Accidentally
connecting multiple pins results in the lowest-order entry being chosen.

   .-----------------------------------------o [11/0xB]
   | .-----------------------------------o [10/0xA]
   | | .------------------------------o [9]
   | | | .-------------------------o [8]
   | | | | .--------------------o [7]
   | | | | | .----------------o [6] x-----o
   | | | | | | .------------o [5] / |
   | | | | | | | .---------o [4] / |
   | | | | | | | | .------o [3] / |
   | | | | | | | | | .---o [2] / |
   | | | | | | | | | | .-o [1] |
   | | | | | | | | | | | o [0] Menu |
   | | | | | | | | | | | |
   | | | | | | | | | | | .-------------'
   | | | | | | | | | | | |
.--+---+---+---+---+---+---+---+---+---+---+---+-----------------------.
| O O O O O O O O O O O O O O O O O |
| 12 11 10 9 8 7 6 5 4 3 2 GND RST RX TX SS MOSI |
| PD6 PB7 PB6 PB5 PB4 PE6 PD7 PC6 PD4 PD0 PD1 PD2 PD1 PB0 PB2 |
| |
| |
|=========# |
| USB # |
| # ARDUINO MICRO |
| MICRO-B # |
|=========# |
| |
| |
| PC7 PF7 PF6 PF5 PF4 PF1 PF0 PB3 PB1 |
| 13 3V3 AREF A0 A1 A2 A3 A4 A5 5V0 RST GND VIN MISO SCK |
| O O O O O O O O O O O O O O O O O |
'--------------+---+---------------------------------------------------'
        | |
        | |
        ?
        /WR_PROT

BINARY MODE:
------------

To choose this mode, pin PF1 needs to be tied to GND or adjacent pad PF0.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PF6 to GND or PF7 (adjacent pad, driving a low level).

Common binary-encoding rotary switches have 10 to 16 positions and connect
the corresponding bit values 1,2,4,8 [LSB..MSB] to the 'C'-contacts; using the
device's binary mode means tieing the four pins PD1..PC6 [LSB..MSB] to GND/0V
as to encode the corresponding boot choices 0(GRUB Menu) up to 15(0xF).
Obviously a proper nerd can also use four separate switches to encode the
choice in binary herself!
(Reminder: The device interprets a pin tied to GND as a '1', so all four
connections mean choice 15/0xF, while no connection means 0.

        .---------------.
        | |
        .--+ 2 --- 4 +--.
        | | / \ | |
        | | C | --> | C +--|-----------.
        | | \ / | | |
        .--|--+ 8 --- 1 +--|-------. |
        | | | | | | |
        | | '---------------' | | |
        | '---------------------|---. | |
        | | | | |
        '--------------------. | | | |
        | | | | |
.------------------------------+---+---+---+---+-----------------------.
| O O O O O O O O O O O O O O O O O |
| 12 11 10 9 8 7 6 5 4 3 2 GND RST RX TX SS MOSI |
| PD6 PB7 PB6 PB5 PB4 PE6 PD7 PC6 PD4 PD0 PD1 PD2 PD1 PB0 PB2 |
| |
| |
|=========# |
| USB # |
| # ARDUINO MICRO |
| MICRO-B # |
|=========# |
| |
| |
| PC7 PF7 PF6 PF5 PF4 PF1 PF0 PB3 PB1 |
| 13 3V3 AREF A0 A1 A2 A3 A4 A5 5V0 RST GND VIN MISO SCK |
| O O O O O O O O O O O O O O O O O |
'--------------+---+-----------+---+-----------------------------------'
        | | | |
        | | '---'
        ? /BM
        /WR_PROT

### Adafruit ItsyBitsy 3V/5V

1-OF-N MODE with ON/OFF/ON toggle switch:
-------------------------------------------

To choose this mode, pin PF1 needs to stay UNCONNECTED.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PF6 to GND or PF7 (adjacent pad, driving a low level).

Using a three-position on/off/on switch permits choosing between two
OS options, while the neutral middle position leads to the GRUB menu

.---------------------------------------------------------.
| O O O O O O O O O O O O O O |
| BAT GND USB 13 12 11 10 9 7 5* SCL SDA TX RX |
| PC7 PD6 PB7 PB6 PB5 PE6 PD0 PD1 PD3 PD2 |
| | ##### [1]
| PD4 4 O | .-----o=# # ////
| | | # #|| ////
|=========# PD7 6 O +--' .--o=# #||//// [0] Menu
| USB # | | # #||
| # ItsyBitsy 3V/5V PB4 8 O +-----|--o=# #
| MICRO-B # | | ##### [2]
|=========# GND O +-----'
| |
| EN O |
| |
| PF7 PF6 PF5 PF4 PF1 PF0 PB1 PB2 PB3 |
| RST * ARf * A0 A1 A2 A3 A4 A5 SCK MOSIMISO * |
| O O O O O O O O O O O O O O |
'------------------+---+----------------------------------'
        | |
        | |
        ?
        /WR_PROT

1-OF-N MODE with rotary switch: (Motto: "This one goes to 11!")
---------------------------------------------------------------

To choose this mode, pin PF1 needs to stay UNCONNECTED.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PF6 to GND or PF7 (adjacent pad, driving a low level).

Common rotary switches have up to 12 positions (some can be limited to fewer
positions with a mechanical keyring). Keeping the first position [0] unconnected
permits choosing the GRUB menu and leaves 11 boot choices, which is the maximum
number of pins sampled. Connecting one of the pins PB4..PB7 to GND
therefore reflects boot choices 1..11 (hexadecimal 0x1..0xB). Accidentally
connecting multiple pins results in the lowest-order entry being chosen.

        .---------------------------------------------o [11/0xB]
        | .---------------------------------------o [10/0xA]
        | | .----------------------------------o [9]
        | | | .-----------------------------o [8]
        | | | | .--------------------o [7]
        | | | | | .----------------o [6] x-----o
        | | | | | | .------------o [5] / |
        | | | | | | | .---------o [4] / |
        | | | | | | | | .----o [3] / |
.----------------------+---+---+---+-------+---+---+---+--. | .-o [2] / |
| O O O O O O O O O O O O O O | | | o [1] |
| BAT GND USB 13 12 11 10 9 7 5* SCL SDA TX RX | | | | o [0] Menu |
| PC7 PD6 PB7 PB6 PB5 PE6 PD0 PD1 PD3 PD2 | | | | |
| | | | | |
| PD4 4 O +--' | | |
| | | | |
|=========# PD7 6 O +------' | |
| USB # | | |
| # ItsyBitsy 3V/5V PB4 8 O +----------' |
| MICRO-B # | |
|=========# GND O +--------------------------'
| |
| EN O |
| |
| PF7 PF6 PF5 PF4 PF1 PF0 PB1 PB2 PB3 |
| RST * ARf * A0 A1 A2 A3 A4 A5 SCK MOSIMISO * |
| O O O O O O O O O O O O O O |
'------------------+---+----------------------------------'
        | |
        | |
        ?
        /WR_PROT

BINARY MODE:
------------

To choose this mode, pin PF1 needs to be tied to GND or adjacent pad PF0.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PF6 to GND or PF7 (adjacent pad, driving a low level).

Common binary-encoding rotary switches have 10 to 16 positions and connect
the corresponding bit values 1,2,4,8 [LSB..MSB] to the 'C'-contacts; using the
device's binary mode means tieing the four pins PB4..PD2 [LSB..MSB] to GND/0V
as to encode the corresponding boot choices 0(GRUB Menu) up to 15(0xF).
Obviously a proper nerd can also use four separate switches to encode the
choice in binary herself!
(Reminder: The device interprets a pin tied to GND as a '1', so all four
connections mean choice 15/0xF, while no connection means 0.

        .---------------.
        | |
        .--+ 2 --- 4 +--.
        | | / \ | |
        | | C | --> | C +--|-----------.
        | | \ / | | |
        .--|--+ 8 --- 1 +--|-------. |
        | | | | | | |
        | | '---------------' | | |
        | '---------------------|---. | |
        | | | | |
        '------------------. | | | |
        | | | | |
.------------------------------------------------------+--. | | | |
| O O O O O O O O O O O O O O | | | | |
| BAT GND USB 13 12 11 10 9 7 5* SCL SDA TX RX | | | | |
| PC7 PD6 PB7 PB6 PB5 PE6 PD0 PD1 PD3 PD2 | | | | |
| | | | | |
| PD4 4 O +--' | | |
| | | | |
|=========# PD7 6 O +------' | |
| USB # | | |
| # ItsyBitsy 3V/5V PB4 8 O +----------' |
| MICRO-B # | |
|=========# GND O +--------------'
| |
| EN O |
| |
| PF7 PF6 PF5 PF4 PF1 PF0 PB1 PB2 PB3 |
| RST * ARf * A0 A1 A2 A3 A4 A5 SCK MOSIMISO * |
| O O O O O O O O O O O O O O |
'------------------+---+-----------+---+------------------'
        | | | |
        | | '---'
        ? /BM
        /WR_PROT
### Sparkfun Pro Micro 3V/5V (and clones)

1-OF-N MODE with ON/OFF/ON toggle switch:
-------------------------------------------

To choose this mode, pin PD2 needs to stay UNCONNECTED.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PF4 to GND or PF5 (adjacent pad, driving a low level).

Using a three-position on/off/on switch permits choosing between two
OS options, while the neutral middle position leads to the GRUB menu

        /WR_PROT
        ?
        | |
        | |
.------------------+---+--------------------------.
| O O O O O O O O O O O O |
| RAW GND RST VCC A3 A2 A1 A0 15 14 16 10 |
| PF4 PF5 PF6 PF7 PB1 PB3 PB2 PB6 |
| |
|=========# |
| USB # |
| # Pro Micro 3.3V/5V |
| MICRO-B # |
|=========# |
| |
| PD3 PD2 PD1 PD0 PD4 PC6 PD7 PE6 PB4 PB5 |
| TXO RXI GND GND 2 3 4 5 6 7 8 9 |
| O O O O O O O O O O O O |
'--------------+---+---+--------------------------'
        | | |
        | | | ##### [1]
        | | '-----------o=# # ////
        | | # #|| ////
        '---|---------------o=# #||//// [0] Menu
        | # #||
        '---------------o=# #
        ##### [2]

1-OF-N MODE with rotary switch: (Motto: "This one goes to 11!")
---------------------------------------------------------------

To choose this mode, pin PD2 needs to stay UNCONNECTED.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PF4 to GND or PF5 (adjacent pad, driving a low level).

Common rotary switches have up to 12 positions (some can be limited to fewer
positions with a mechanical keyring). Keeping the first position [0] unconnected
permits choosing the GRUB menu and leaves 11 boot choices, which is the maximum
number of pins sampled. Connecting one of the pins PD1..PB3 to GND
therefore reflects boot choices 1..11 (hexadecimal 0x1..0xB). Accidentally
connecting multiple pins results in the lowest-order entry being chosen.

        /WR_PROT .--------------------.
        ? | .-------------. |
        | | | | .------. | |
        | | | | | | | |
.------------------+---+---------------+---+---+--. | | |
| O O O O O O O O O O O O | | | |
| RAW GND RST VCC A3 A2 A1 A0 15 14 16 10 | | | |
| PF4 PF5 PF6 PF7 PB1 PB3 PB2 PB6 | | | |
| | | | |
|=========# | | | |
| USB # | | | |
| # Pro Micro 3.3V/5V | | | |
| MICRO-B # | | | |
|=========# | | | |
| | | | |
| PD3 PD2 PD1 PD0 PD4 PC6 PD7 PE6 PB4 PB5 | | | |
| TXO RXI GND GND 2 3 4 5 6 7 8 9 | | | |
| O O O O O O O O O O O O | | | o [11/0xB]
'--------------+---+---+---+---+---+---+---+---+--' | 'o [10/0xA]
        | | | | | | | | | '--o [9]
        | | | | | | | | '--------o [8]
        | | | | | | | '-----------o [7]
        | | | | | | '---------------o [6] x-----o
        | | | | | '-------------------o [5] / |
        | | | | '------------------------o [4] / |
        | | | '-----------------------------o [3] / |
        | | '----------------------------------o [2] / |
        | '----------------------------------------o [1] |
        | o [0] Menu |
        | |
        '------------------------------------------------------------'

BINARY MODE:
------------

To choose this mode, pin PD2 needs to be tied to the adjacent GND pin.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PF4 to GND or PF5 (adjacent pad, driving a low level).

Common binary-encoding rotary switches have 10 to 16 positions and connect
the corresponding bit values 1,2,4,8 [LSB..MSB] to the 'C'-contacts; using the
device's binary mode means tieing the four pins PD1..PC6 [LSB..MSB] to GND/0V
as to encode the corresponding boot choices 0(GRUB Menu) up to 15(0xF).
Obviously a proper nerd can also use four separate switches to encode the
choice in binary herself!
(Reminder: The device interprets a pin tied to GND as a '1', so all four
connections mean choice 15/0xF, while no connection means 0.

        /WR_PROT
        ?
        | |
        | |
.------------------+---+--------------------------.
| O O O O O O O O O O O O |
| RAW GND RST VCC A3 A2 A1 A0 15 14 16 10 |
| PF4 PF5 PF6 PF7 PB1 PB3 PB2 PB6 |
| |
|=========# |
| USB # |
| # Pro Micro 3.3V/5V |
| MICRO-B # |
|=========# |
| |
| PD3 PD2 PD1 PD0 PD4 PC6 PD7 PE6 PB4 PB5 |
| TXO RXI GND GND 2 3 4 5 6 7 8 9 |
| O O O O O O O O O O O O |
'------+---+---+---+---+---+---+------------------'
       | | | | | | |
       '---' | | | | '-----------------------.
        /BM | | | | |
        | | '---|-----------------------. |
        | | | | |
        | | | .---------------. | |
        | | | | | | |
        | '-------|---+ 1 --- 8 +---|---'
        | | | / \ | |
        '-----------|---+ C | <-- | C | |
        | | \ / | |
        '---+ 4 --- 2 +---'
        | |
        '---------------'

### DFRobot Beetle

1-OF-N MODE with ON/OFF/ON toggle switch:
-------------------------------------------

To choose this mode, pin PB6 needs to stay UNCONNECTED.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PB7 to GND.

Using a three-position on/off/on switch permits choosing between two
OS options, while the neutral middle position leads to the GRUB menu

        .-------------------.
        | |
     ___________ _____ _____ | ____ |
    | | | \___/ \___/ \_|_/ | |
    | -+5V- | O O O _|_ | ##### [1]
    | | | A2 A1 A0 / \ '---o=# # ////
    |-------/ PF5 PF6 PF7 / | \ # #|| ////
    | | GND |------------o=# #||//// [0] Menu
|=========# \ | /| # #||
| USB # \___/ | .---o=# #
| # DFRobot Beetle ___ | | ##### [2]
| MICRO-B # / \ | |
|=========# / | \| |
    | | -+5V- | |
    |-------\ PB7 PB6 PB5 \ | / |
    | | | D11 D10 D9 \___/ |
    | GND | _O_ _O_ _O_ | |
    |___|___|___/ | \_____/ \_____/ | \____| |
        | | | |
        | | | |
        | /WR_PROT| '-------------------'
        ?

1-OF-N MODE with rotary switch: (Motto: "This one goes to 11!")
---------------------------------------------------------------

To choose this mode, pin PB6 needs to stay UNCONNECTED.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PB7 to GND.

Common rotary switches have up to 12 positions (some can be limited to fewer
positions with a mechanical keyring). Keeping the first position [0] unconnected
permits choosing the GRUB menu and in principle leaves 11 boot choices, however
Beetle only has 8 accessible connection points left, side pads PB5..BF5 for
positions [1]..[4] and the PCB bottom pads PD0..PD3 for positions [5]..[8]
Connecting one of those pads to GND through the switch reflects the boot
choices 1..8. Accidentally connecting multiple pins results in the lowest-order
entry being chosen.

        o [11/0xB]
        o [10/0xA]
        o [9]
        PD3/TX O--------o [8]
        PD2/RX O-------o [7]
        PD1/SDA O-------o [6] x-----o
        PD0/SCL O-------o [5] / |
        .--------------------------------o [4] / |
        | .-----------------------o [3] / |
        | | .--------------o [2] / |
     ___________ | _____ | _____ | ____ .-o [1] |
    | | | \_|_/ \_|_/ \_|_/ | | o [0] Menu |
    | -+5V- | O O O _|_ | |
    | | | A2 A1 A0 / \ | |
    |-------/ PF5 PF6 PF7 / | \ | |
    | | GND |---|-----------------'
|=========# \ | /| |
| USB # \___/ | |
| # DFRobot Beetle ___ | |
| MICRO-B # / \ | |
|=========# / | \| |
    | | -+5V- | |
    |-------\ PB7 PB6 PB5 \ | / |
    | | | D11 D10 D9 \___/ |
    | GND | _O_ _O_ _O_ | |
    |___|___|___/ | \_____/ \_____/ | \____| |
        | | | |
        | | | |
        | /WR_PROT| '--------------'
        ?

BINARY MODE:
------------

To choose this mode, pin PB6 needs to be tied to GND.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PB7 to GND.

Common binary-encoding rotary switches have 10 to 16 positions and connect
the corresponding bit values 1,2,4,8 [LSB..MSB] to the 'C'-contacts; using the
device's binary mode means tieing the four pins PB5..PF5 [LSB..MSB] to GND/0V
as to encode the corresponding boot choices 0(GRUB Menu) up to 15(0xF).
Obviously a proper nerd can also use four separate switches to encode the
choice in binary herself!
(Reminder: The device interprets a pin tied to GND as a '1', so all four
connections mean choice 15/0xF, while no connection means 0.

        .---------------.
        | |
      .--+ 2 --- 4 +--.
      | | / \ | |
      | | C | --> | C +--|------------------------.
      | | \ / | | |
   .--|--+ 8 --- 1 +--|------------------------|---.
   | | | | | | |
   | | '---------------' | | |
   | '---------------------|---------. | |
   | | | | |
   '--------------. | | | |
        | | | | |
        | | | | |
     ___________ | _____ | _____ | ____ | |
    | | | \_|_/ \_|_/ \_|_/ | | |
    | -+5V- | O O O _|_ | |
    | | | A2 A1 A0 / \ | |
    |-------/ PF5 PF6 PF7 / | \ | |
    | | GND |---' |
|=========# \ | /| |
| USB # \___/ | |
| # DFRobot Beetle ___ | |
| MICRO-B # / \ | |
|=========# / | \| |
    | | -+5V- | |
    |-------\ PB7 PB6 PB5 \ | / |
    | | | D11 D10 D9 \___/ |
    | GND | _O_ _O_ _O_ | |
    |___|___|___/ | \_____/ | \_____/ | \____| |
        | | | | |
        | | | | |
        | /WR_PROT| | '------------------'
        | ? |
        | |
        | |
        '-------------------'
        /BM
### PJRC Teensy 2.0

1-OF-N MODE with ON/OFF/ON toggle switch:
-------------------------------------------

To choose this mode, pin PB6 needs to stay UNCONNECTED.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PF4 to GND or PF1 (adjacent pad, driving a low level).

Using a three-position on/off/on switch permits choosing between two
OS options, while the neutral middle position leads to the GRUB menu

        /WR_PROT
        ?
        | |
        | |
.----------+---+---------------------------------.
| O O O O O O O O O O O O |
| VCC F0 F1 F4 F5 F6 F7 B6 B5 B4 D7 D6 |
| |
| D4 O |
| |
|========# RST O |
| USB # |
| # Teensy 2.0 GND O |
| MINI-B # |
|========# VCC O |
| |
| D5 O |
| |
| GND B0 B1 B2 B3 B7 D0 D1 D2 D3 C6 C7 |
| O O O O O O O O O O O O |
'--+---+---+-------------------------------------'
   | | |
   | | |
   | | |
   | | | ##### [1]
   | | '----------------------------o=# # ////
   | | # #|| ////
   '---|--------------------------------o=# #||//// [0] Menu
       | # #||
       '--------------------------------o=# #
        ##### [2]

1-OF-N MODE with rotary switch: (Motto: "This one goes to 11!")
---------------------------------------------------------------

To choose this mode, pin PB6 needs to stay UNCONNECTED.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PF4 to GND or PF1 (adjacent pad, driving a low level).

Common rotary switches have up to 12 positions (some can be limited to fewer
positions with a mechanical keyring). Keeping the first position [0] unconnected
permits choosing the GRUB menu and leaves 11 boot choices, which is the maximum
number of pins sampled. Connecting one of the pins PB0..PC7 to GND
therefore reflects boot choices 1..11 (hexadecimal 0x1..0xB). Accidentally
connecting multiple pins results in the lowest-order entry being chosen.

        /WR_PROT
        ?
        | |
        | |
.----------+---+---------------------------------.
| O O O O O O O O O O O O |
| VCC F0 F1 F4 F5 F6 F7 B6 B5 B4 D7 D6 |
| |
| D4 O |
| |
|========# RST O |
| USB # |
| # Teensy 2.0 GND O |
| MINI-B # |
|========# VCC O |
| |
| D5 O |
| |
| GND B0 B1 B2 B3 B7 D0 D1 D2 D3 C6 C7 |
| O O O O O O O O O O O O |
'--+---+---+---+---+---+---+---+---+---+---+---+-'
   | | | | | | | | | | | |
   | | | | | | | | | | | '------o [11/0xB]
   | | | | | | | | | | '--------o [10/0xA]
   | | | | | | | | | '-----------o [9]
   | | | | | | | | '--------------o [8]
   | | | | | | | '-----------------o [7]
   | | | | | | '---------------------o [6] x-----o
   | | | | | '-------------------------o [5] / |
   | | | | '------------------------------o [4] / |
   | | | '-----------------------------------o [3] / |
   | | '----------------------------------------o [2] / |
   | '----------------------------------------------o [1] |
   | o [0] Menu |
   '------------------------------------------------------------------'

BINARY MODE:
------------

To choose this mode, pin PB6 needs to be tied to GND or adjacent pad PB5.

The Write Protect against modifying boot entry configurations is activated
by tieing/jumpering pin PF4 to GND or PF1 (adjacent pad, driving a low level).

Common binary-encoding rotary switches have 10 to 16 positions and connect
the corresponding bit values 1,2,4,8 [LSB..MSB] to the 'C'-contacts; using the
device's binary mode means tieing the four pins PB0..PB3 [LSB..MSB] to GND/0V
as to encode the corresponding boot choices 0(GRUB Menu) up to 15(0xF).
Obviously a proper nerd can also use four separate switches to encode the
choice in binary herself!
(Reminder: The device interprets a pin tied to GND as a '1', so all four
connections mean choice 15/0xF, while no connection means 0.

        /WR_PROT
        ? /BM
        | | .---.
        | | | |
.----------+---+---------------+---+-------------.
| O O O O O O O O O O O O |
| VCC F0 F1 F4 F5 F6 F7 B6 B5 B4 D7 D6 |
| |
| D4 O |
| |
|========# RST O |
| USB # |
| # Teensy 2.0 GND O |
| MINI-B # |
|========# VCC O |
| |
| D5 O |
| |
| GND B0 B1 B2 B3 B7 D0 D1 D2 D3 C6 C7 |
| O O O O O O O O O O O O |
'--+---+---+---+---+-----------------------------'
   | | | | |
   | | | | '-----------------------.
   | | | | |
   | | '---|-----------------------. |
   | | | | |
   | | | .---------------. | |
   | | | | | | |
   | '-------|---+ 1 --- 8 +---|---'
   | | | / \ | |
   '-----------|---+ C | <-- | C | |
        | | \ / | |
        '---+ 4 --- 2 +---'
        | |
        '---------------'

### The GRUB SWITCH Custom Hardware

For the switch connection options available for our custom hardware PCB, please refer to its full documentation in
grub-switch/documentation/3_custom_hardware.pdf