The GRUB Switch
Custom Hardware Rev. B
Ruediger Willenberg
Version 1.0
May 15, 2021

# GRUB Switch sources (incl. hardware)
The executable or compilable GRUB Switch files and sources are designed to be installed and used under Linux, however the files for our custom PCB (EAGLE files, Gerber files and documentation images, PDFs and Open Document files) are relative platform-independent.
There are two ways to obtain the files:
- Via git clone:
  - Go to your preferred working directory
  - Clone the repository with
    git clone https://github.com/rw-hsma-fpga/grub-switch.git
  - All GRUB Switch files are now available in the path
    ./grub-switch
- Via download:
  - Download to your preferred directory:
    https://github.com/rw-hsma-fpga/grub-switch/archive/refs/heads/master.zip
  - Unzip with GUI-tool or on the command line with
    unzip grub-switch-master.zip
  - All GRUB Switch files are now available in the path
    ./grub-switch-master

All further examples will assume you are starting in the parent directory above grub-switch
All data directly related to the PCB design and components are in
grub-switch/3_custom_hardware/
while this document itself is in
grub-switch/documentation/
# Introduction
## Motivation
The GRUB Switch Custom HW (Revision B) was designed with an eye on the following unique features:
- An independent, open source, PCB design that can be self-assembled
- Firmware programmable via USB with the factory-state ATmega32u4 MCU, without having to install a custom bootlader.
- Featuring soldering pads for the two most useful electromechanical switch options, common 1x12 rotary switches and DPDT toggle switches. Both commonly offer mounting threads, so the entire PCB can be mounted directly into a front panel or PC case. No cable or wire soldering required.
- Regular USB socket, but also the option to directly connect internally to a PC motherboard, pin header-to-pin header via standard ribbon cable.
- Write-protect switch or jumper to block tampering with the boot configuration
On top of this, the board can be used for any other embedded design purposes separate from GRUB Switch, as 13 I/O pins are exposed as solder pads. In principle, any valid ATmega32u4 firmware should be able to run (see last section).
## File structure
There are 3 subdirectories in grub-switch/3_custom_hardware:
./bill_of_materials: Complete component list in ODS (Open Document Spreadsheet) and PDF formats, with multiple alternatives for some components. Order codes for two international distributors are included for convenience, but do not constitute an endorsement.
./eagle_files: Autodesk EAGLE *.brd and *.sch files, saved with version 9.6.2, but likely downwards compatible to at least version 8.x. Size and features conform to be viewable and editable with a free version of EAGLE. All components included without library files.
Further, PDF versions of the schematic as well as top and bottom layer views with dimension, pads, vias, components and silkscreen.
./gerber_files: Gerber RS274-X and NC drill files that should work with most low-cost PCB manufacturers.
## Description
The PCB board is a 2-layer (top/bottom) design with external dimensions of 68x25mm. It it designed for standard 1.6mm board thickness; variations should be unproblematic, but in that case keep an eye on the mounting depth of the rotary or toggle switches as well as the Molex USB-Mini-B receptacle.
The board has no wire with less than 8mil width and only fully drilled, round solder pads and vias, with the exception of two oval mounting pads for the Molex USB Mini-B receptacle.
All components except for the rotary or toggle switches are mounted on the top layer side.

Top layer view:

Bottom layer view:

# Components info
Also see the bill of materials for details and order options.
## Single-manufacturer/proprietary components
### Atmel/Microchip ATmega32U4-AU (essential)
The MCU being used in this design is the version in a TQFP-44 package without an internal RC oscillator.
Do NOT use the ATmega32U4RC-AU version because it has different fuse settings and the factory-state firmware programming will not work with our board.
Do NOT use the ATmega32U4-MU version because it has a different package size and won’t fit the footprint. It also does not have the pre-installed bootloader.
### Molex USB Mini-B receptacle, through-hole, vertical, Part No. 502237-0517 (optional)
This is another entirely proprietary component, with no other vendor offering a compatible mounting and solder pad pattern. However it is not an essential component as you can use the 1x5 pinheader next to it to connect to USB, especially on internally mounted designs (also see the section on saving part costs).
### Würth WS-SLTU THT Mini Slide Switch for Write-Protect (optional)
While the board is designed for this right-angled mini slide-switch to fit snugly on the PCB side, its through-hole pads have a common 2.54mm (1/10”) pitch and might be replacable with other small switches (be aware of the 0,8mm padhole diameter).
Alternatively, the board has a parallel 1x2 pinheader that can be used for a Write-Protect jumper instead (also see the section on saving part costs).
## Non-proprietary components
### Crystal 16Mhz
Our bill of materials already lists 5 commonly available models, but there are likely others that fit the required specs:
- Frequency: 16Mhz, load capacitance: 18pF
- Size 5.0x3.2mm with 2 SMD pads (careful, there are incompatible 4-pad versions!)
- Both tolerance and ESR variations for other available models should not be critical.
### PTS647 push button / tactile switch 4.5x4.5mm
There are very likely other switches with a compatible footprint. This switch is also replacable by another solution to short the 1x2 pin header contacts labeled PROG.
### Osram LG R971-KN-1 ChipLED (SMD-0805)
The LED can be replace by any other 0805 format chip LED, but take care to choose the right series resistor value for R8 (currently 1k) to get the proper forward current for the LED. The pin voltage level for ON is 5V. While the I/O pins can source double-digit mA currents, we suggest staying in the single-digit mA range.
### Resistors and Capacitors (SMD-0805)
There are, of course, plenty of other 0805 format resistors and capacitors you can use; respect the parameters for value, tolerance, dielectric material and maximum voltage in the bill of materials, though.
### Boot choice switches
See the bill of materials and section on switch wiring below for details
## Saving money on component cost
The most expensive components that are essential are the PCB (see comments below), the MCU, the crystal and the rotary or toggle switches you use. Nothing to be done there.
PCB manufacturing in East Asia is actually really cheap, but the per-board cost is only small if you need multiple boards and/or can minimize the shipping costs (which means waiting longer). Maybe you can pool an order with other people.
Expensive components that are non-essential are:
- The Molex USB Mini-B receptacle. You can use the 1x5 USB pinheader and a ribbon cable, especially if you’re wiring internally to a PC motherboard.
- The Würth slide switch – you can use the 1x2 pinheader and jumper it for Write-Protect, or even short the corresponding solder bridge if you don’t want to ever change your configuration again (really sure??)
- You can use the PROG 1x2 pin header pads (w/ or w/o pinheader) to enter bootloader mode instead of the push button. Make sure to disconnect cleanly to get the proper /RST and /HWB timing.
- Who needs an LED indicator if everything works as advertised?

# Placement and soldering info
While we tried to make components as big as possible without compromising too much on PCB size, at least a magnifier and possibly a soldering microscope is useful.
We recommend to place and solder the components in the following order:
1. The Atmega MCU: Make sure that pin 1 marker is in the right spot (see next page) and that no two pins are shorted with solder. Copper soldering mesh is great to draw excess solder out again under heat.
2. The crystal. This is a bit hard because part some of the solder is supposed to be on the side of the case and some is supposed to flow under the case. Put only a small dollop of solder on one pad, then place the component symmetrically with pincers while heating the solder again. When the solder cooled and the crystal is fixed, solder the second pad.
3. The resistors (see color-coded placement pattern on the following page)
4. The capacitors (see image again)
5. The LED. Check twice for anode/cathode direction.
6. The WR_PROT slide switch (if required). Nothing ist standing far out yet, so you can solder the pins on the bottom layer side while the switch is pressed flat between the table and the board. Center pins well inside the pad hole so the slide is snug on the PCB side.
7. The Mini-USB Mini-B receptacle (if required). Make sure all 5 USB contacts go through the holes. Solder the high-mass (lots of heat) mechanical contacts first, then the USB contacts.
8. The PROG push button
9. Any pin headers (USB 1x5, WR_PROT 1x2, PROG 1x2) you require.
10. See the section on boot switch options at the end for
It is fairly simple to adapt the firmware to another board with the ATmega32u4 and build a firmware image. See the detailed documentation for instructions.

## Programming the boards with GRUB Switch firmware
On the Linux command-line, go to the grub-switch/2_usb_device/prebuilt_images directory, where you can find the suitable image and programming scripts.
### THE GRUB SWITCH custom USB hardware Rev.B
Our custom USB device design relies on the DFU bootloader which is factory-built into each ATmega32u4 chip. There is an open source command-line tool called dfu-programmer which needs to be installed for firmware flashing.
- Under Ubuntu Linux, it can be installed with:
  sudo apt-get install dfu-programmer
- To simplify the use of dfu-programmer, we have provided a script in prebuilt_images. After plugging in your board, it can be started with:
  sudo ./program_grubswitch_dfu.sh GRUB_SWITCH_CUSTOMHW_REVB.hex
  (The use of sudo might not be required on your installation)
- Before or after starting the script, the chip needs to be brought into bootloader mode by pushing or shorting the PROG button. Unlike the Arduino boards, there is no bootloader timeout. Pressing a key on the keyboard will start programming.
After successful firmware programming, the board identifies as a FAT storage device with the drive name BOOTTHIS. Depending on your Linux GUI, you might get a notification.
## Writing the GRUB Switch boot configuration onto your storage device
Together with the boot.* directories, option 2 of the CONFIGURE_GRUBswitch.sh script has also written a single text file holding the complete list and order of boot choices:
bootfiles/.entries.txt
You can open with a text editor to see the ordered list of boot choices, however it is not recommended to edit the file by hand. Because the filename starts with a period, it is only visible if you use the -a option with ls:
ls -la bootfiles/
If you mount your USB storage device automatically through the GUI, you can just copy the file onto the device and unmount again.
Alternatively, you can use option 4 - Write GRUBswitch bootfile to GRUBswitch USB device in the CONFIGURE_GRUBswitch.sh tool. This requires giving the sudo password because the mounting and unmounting of the device is being forced.
NOTE: Your USB device is not a regular flash drive. .entries.txt is the only file that will be accepted for writing, and only if the Write-Protect jumper is not set on the board (see wiring section). The only other (read-only) files on the device are:
SWITCH.GRB – The actual boot setting script read by GRUB. If there are no switch connections on the board yet, this will be empty because that is the default leading to the GRUB menu.
.bootpins.txt – This file (also hidden without ls -a) shows the choice pins currently connected to GND as ones. It is only included for testing purposes.
### The GRUB SWITCH Custom Hardware Revision B
Our custom PCB has been designed with an eye to directly mounting and soldering two common types of switches for 1-of-n mode (shorting one single choice pin to ground at a time).
The silhouettes for both a 1-of-12 rotary switch and a on/off/on toggle switch are visible on the PCB side titled with “THE GRUB SWITCH” (the bottom layer in the PCB files). The switches are supposed to be through-hole-mounted on this side (which means they will be soldered on the side labeled with “1/n-mode”). Therefore, this is also the side facing the front panel of a case.
Because both types of switches are available with a screw thread for front-panel mounting, the PCB and switch can be affixed mechanically to a case.

##### 1-of-n mode with ON/OFF/ON switch
The rectangular white silhouette shows the mounting position for a two-channel on/off/on toggle switch (DPDT - ”double-pole/double-throw”). Only the upper channel is actually used; the two channel model was chosen to decrease mechanical stress on solder pads and increase stability.
The pad numbers 1 and 2 indicate the boot choices made through electrical connection to the center pad. Note that the toggle switch lever moves across a fixed pivot, so moving the lever to the left (as seen from the front) actually connects choice 2, while moving the lever to the right chooses boot option 1. The neutral center position leads to the GRUB menu.
The following toggle switch series include DPDT on/off/on models with the required 4.7-4.75mm distance between PCB pins:
APEM Series 5000	E-Switch Series 100
NKK Series M	TE-Connectivity Gemini A
(these suggestions should not be considered a commercial endorsement)
##### 1-of-n mode with 1-of-12 rotary switch
The round silhouette indicates the mounting position of a 1-of-12 rotary switch. On the PCB side labeled with “1/n-mode” the 11 switch positions for boot choices of increasing order are indicated; position 0 leads to the menu. Because the switch is mounted on the other PCB side, choices increase by turning the switch clockwise.
The switch’s main connection pin, which is tied to GND, shares a pad with the toggle switch and is indicated by an octagonal silhouette. It is not in the center of the rotary switch, therefore the switch can only be mounted in exactly one position.
Compatible rotary switches with various actuator shapes and lengths, as well as metric and imperial mounting holes and threads, are available from multiple vendors:
C&K A112.**.*.NC.**	E-Switch KC52.*.***.**.NP.*
LORLIN CK1049/CK1059 (metric), CK1044/CK1054 (imperial)
(these suggestions should not be considered a commercial endorsement)
Make sure to order the 1x12 variation, as there are also 2x6, 3x4 and 4x3 models. Most switches come with a metal keyring that can be inserted before tightening the screw and that will limit the range of movement to less than 12 steps; so if you only need, say, 4 boot choices including the GRUB menu option, the range of movement can be fixed to 4 steps.
##### Binary mode
The Custom PCB isn’t designed to hold a binary-encoding switch, but binary mode can be selected anyway by connecting the solder bridge marked with “Binary mode”. The numbers
1, 2, 4, 8 inside the round silhouette indicate the pads to connect to GND to choose the corresponding power of 2. GND level is available at the pad marked with an octagonal silhoutte.
##### Write-protect
A fully-equipped board should include a slide switch to enable and disable write-protect for the boot configuration file. Two alternatives are:
- Write-protect can be enabled permanently by connecting the solder bridge marked with a rectangle next to the WR_PROT label.
- Next ot the solder bridge are pads for a 1x2 pin header, which can be jumpered to enable write-protect non-permanently.